## Slide 1: CSC 112: Computer Operating Systems Lecture 5 Scheduling Exercises Solution
Department of Computer Science,
Hofstra University
Acknowledgement: Lecture slides based on UC Berkeley CS 162: Operating Systems and System Programming

## Slide 2: Predicting Burst Time
Use exponential averaging n = tn-1+(1-)n-1 to predict the next burst time. Assume initial estimate 0 = 10, and the actual burst times of the first four processes t0, t1, t2, t3 are 4, 8, 6 and 7, respectively. Given α = 0.5. Compute the predicted burst times 1, 2, 3, 4.

## Slide 3: Predicting Burst Time ANS
Use exponential averaging to predict the next burst time. Assume initial estimate t0 = 10, and the actual burst times of the first four processes x1, x2, x3, x4 are 4, 8, 6 and 7, respectively. Given α = 0.5. Compute the predicted burst times t1, t2, t3, t4. (It is best if you can bring a calculator. But if you do not have one, just writing out the following formulas is OK.)
1 = 0.5 x 4 + 0.5 x 10 = 7
2 = 0.5 x 8 + 0.5 x 7 = 7.5
3 = 0.5 x 6 + 0.5 x 7.5 = 6.75
4 = 0.5 x 7 + 0.5 x 6.75 = 6.875

## Slide 4: Scheduling
Here is a table of processes and their arrival and execution times.
1) Draw the Gantt chart under 4 policies: First Come First Serve (FCFS), Shortest Job First (SJF), Shortest-Remaining-Time-First (SRTF), Round-Robin (RR) with time quantum = 1. Assume that context switch overhead is 0. For RR, assume that an arriving process is scheduled to run at the beginning of its arrival time, i.e., it is added to the head of the queue upon arrival.
2) Compute the finish times and response times for all processes, and the average response time. (If the division is hard, write a fraction like 28/5 instead of 5.6)

## Slide 5: Scheduling I
PID | Arriv. time | Exec Time | FCFS Finish Time | FCFS Response Time | SJF Finish Time | SJF Response Time | SRTF Finish Time | SRTF Response Time | RR Finish Time | RR Response Time
1 | 0 | 2 |  |  |  |  |  |  |  | 
2 | 1 | 6 |  |  |  |  |  |  |  | 
3 | 4 | 2 |  |  |  |  |  |  |  | 
 |  | Average Turnaround |  | Avg RT |  | Avg RT |  | Avg RT |  | Avg RT
FCFS |  |  |  |  |  |  |  |  |  | 
SJF |  |  |  |  |  |  |  |  |  | 
SRTF |  |  |  |  |  |  |  |  |  | 
RR |  |  |  |  |  |  |  |  |  | 
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Gantt Chart

## Slide 6: Scheduling I ANS
PID | Arriv. time | Exec Time | FCFS Finish Time | FCFS Response Time | SJF Finish Time | SJF Response Time | SRTF Finish Time | SRTF Response Time | RR Finish Time | RR Response Time
1 | 0 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3
2 | 1 | 6 | 8 | 7 | 8 | 7 | 10 | 9 | 10 | 9
3 | 4 | 2 | 10 | 6 | 10 | 6 | 6 | 2 | 7 | 3
 |  | Average Turnaround |  | Avg RT 5 |  | Avg RT 5 |  | Avg RT 4.3 |  | Avg RT 5
FCFS | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3
SJF | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3
SRTF | 1 | 1 | 2 | 2 | 3 | 3 | 2 | 2 | 2 | 2
RR | 1 | 2 | 1 | 2 | 3 | 2 | 3 | 2 | 2 | 2
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Gantt Chart
P1 arrival
P2 arrival
P3 arrival
Response time = FinishTime – ArrivalTime

## Slide 7: Scheduling II
PID | Arriv. time | Exec Time | FCFS Finish Time | FCFS Response Time | SJF Finish Time | SJF Response Time | SRTF Finish Time | SRTF Response Time | RR Finish Time | RR Response Time
1 | 0 | 3 |  |  |  |  |  |  |  | 
2 | 1 | 5 |  |  |  |  |  |  |  | 
3 | 3 | 2 |  |  |  |  |  |  |  | 
4 | 9 | 2 |  |  |  |  |  |  |  | 
 |  | Average Turnaround |  | Avg RT |  | Avg RT |  | Avg RT |  | Avg RT
FCFS |  |  |  |  |  |  |  |  |  |  |  | 
SJF |  |  |  |  |  |  |  |  |  |  |  | 
SRTF |  |  |  |  |  |  |  |  |  |  |  | 
RR |  |  |  |  |  |  |  |  |  |  |  | 
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Gantt Chart

## Slide 8: Scheduling II ANS
PID | Arriv. time | Exec Time | FCFS Finish Time | FCFS Response Time | SJF Finish Time | SJF Response Time | SRTF Finish Time | SRTF Response Time | RR Finish Time | RR Response Time
1 | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 6 | 6
2 | 1 | 5 | 8 | 7 | 10 | 9 | 10 | 9 | 11 | 10
3 | 3 | 2 | 10 | 7 | 5 | 2 | 5 | 2 | 7 | 4
4 | 9 | 2 | 12 | 3 | 12 | 3 | 12 | 3 | 12 | 3
 |  | Average Turnaround |  | Avg RT 5 |  | Avg RT 4.25 |  | Avg RT 4.25 |  | Avg RT 5.75
FCFS | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 4 | 4
SJF | 1 | 1 | 1 | 3 | 3 | 2 | 2 | 2 | 2 | 2 | 4 | 4
SRTF | 1 | 1 | 1 | 3 | 3 | 2 | 2 | 2 | 2 | 2 | 4 | 4
RR | 1 | 2 | 1 | 3 | 2 | 1 | 3 | 2 | 2 | 4 | 2 | 4
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Gantt Chart
P1 arrival
P2 arrival
P3 arrival
P4 arrival
Response time = FinishTime – ArrivalTime

## Slide 9: Scheduling II ANS (RR Explanation)
FCFS | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 4 | 4
SJF | 1 | 1 | 1 | 3 | 3 | 2 | 2 | 2 | 2 | 2 | 4 | 4
SRTF | 1 | 1 | 1 | 3 | 3 | 2 | 2 | 2 | 2 | 2 | 4 | 4
RR | 1 | 2 | 1 | 3 | 2 | 1 | 3 | 2 | 2 | 4 | 2 | 4
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Gantt Chart
P1 arrival
P2 arrival
P3 arrival
P4 arrival
RR scheduling explanations:
Time 1: P2 arrives, and it runs immediately based on our assumption that an arriving process is added to the head of the queue upon arrival.
Time 3: P3 arrives, and it runs immediately.
Time 4: P2 runs since it is next in ready queue based on the cyclic pattern of “12, 12”.
Time 6: P3 runs based on the cyclic pattern of “321, 321”.
Time 9: P4 arrives, and it runs immediately.

## Slide 10: Scheduling III
Consider the set of 3 processes whose arrival time and CPU burst times are given below. If the CPU scheduling policy is FCFS, draw the Gantt chart and calculate the average response time.
PID | Arriv. time | Exec Time | FCFS Finish Time | FCFS Response Time
1 | 0 | 2 |  | 
2 | 3 | 1 |  | 
3 | 5 | 6 |  | 
 |  | Average Turnaround |  | Avg RT

## Slide 11: Scheduling III ANS
PID | Arriv. time | Exec Time | FCFS Finish Time | FCFS Response Time
1 | 0 | 2 | 2 | 2
2 | 3 | 1 | 4 | 1
3 | 5 | 6 | 11 | 6
 |  | Average Turnaround |  | Avg RT 3
Gantt Chart
P1 arrival
P2 arrival
P3 arrival

## Slide 12: Scheduling with Bursts I
Consider the set of 3 processes whose arrival time and CPU/IO burst times are given below. If the CPU scheduling policy is Shortest Remaining Time First (SRTF), draw the Gantt chart and calculate the average response time. (Note: consider the overlap of computation and IO bursts of different processes)
PID | Arriv. time | IO Burst | CPU Burst | IO Burst
1 | 0 | 2 | 7 | 1
2 | 0 | 4 | 14 | 2
3 | 0 | 6 | 21 | 3
 |  |  |  | Avg RT

## Slide 13: Scheduling with Bursts I ANS
PID | Arriv. time | IO Burst | CPU Burst | IO Burst | Finish Time | Resp. Time
1 | 0 | 2 | 7 | 1 | 10 | 10
2 | 0 | 4 | 14 | 2 | 25 | 25
3 | 0 | 6 | 21 | 3 | 47 | 47
 |  |  |  |  | Avg RT | 27.3
IO
IO
IO
IO
IO
IO
P1, P2, P3 arrival
Time 2: active tasks’ remaining times: P1: 7
Time 4: active tasks’ remaining times: P1: 5, P2: 14, so P1 continues to run
Time 6: active tasks’ remaining times: P1: 3, P2: 14, P3: 21, so P1 continues to run
Time 9: active tasks’ remaining times: P2: 14, P3: 21, so P2 starts to run (P1 is blocked for IO)
Time 10: active tasks’ remaining times: P2: 13, P3: 21, so P2 continues to run (P1 is finished)
Time 23: active tasks’ remaining times: P3: 21, so P3 starts to run (P2 is blocked for IO)

## Slide 14: Scheduling with Bursts II
Consider the set of 3 processes whose arrival time and CPU/IO burst times are given below. If the CPU scheduling policy is Fixed-Priority Scheduling (larger number denotes higher priority), draw the Gantt chart and calculate the average response time.
PID | Arriv. time | Priority | CPU Burst | IO Burst | CPU Burst
1 | 0 | 2 | 1 | 5 | 3
2 | 2 | 1 | 3 | 3 | 1
3 | 3 | 3 | 2 | 3 | 1
 |  |  | Avg RT |  | Avg RT

## Slide 15: Scheduling with Bursts II ANS
PID | Arriv. time | Priority | CPU Burst | IO Burst | CPU Burst | Finish Time | Resp. Time
1 | 0 | 2 | 1 | 5 | 3 | 10 | 10
2 | 2 | 1 | 3 | 3 | 1 | 15 | 13
3 | 3 | 3 | 2 | 3 | 1 | 9 | 6
 |  |  |  |  |  | Avg RT | 9.67
IO
IO
IO
P1 arrival
P2 arrival
P3 arrival
For fixed-priority scheduling, draw the Gantt chart starting from highest priority process and go down to the lowest priority (first P3, then P1, then P2). Schedule CPU bursts of lower priority processes in the remaining time slots that are left over by higher priority processes.