## Slide 1: CSC 112: Computer Operating Systems Lecture 6 Real-Time Scheduling Exercises
Department of Computer Science,
Hofstra University

## Slide 2: Q1. Schedulability under RM or EDF
Determine schedulability of the following tasksets under (1) Rate Monotonic (RM) scheduling, using Utilization Bound test and/or Response Time Analysis (RTA) to determine taskset schedulability. (2) Earliest Deadline First (EDF) scheduling, using Utilization Bound test. We use the notation i (Ci, Ti, Di) to denote task i with WCET Ci, Period Ti, Deadline Di (c.f. Slide 33 in Lecture 6)
1) Taskset 1 (3, 6, 6), 2 (4, 9, 9)
2) Taskset 1 (3, 6, 6), 2 (3, 9, 9)
3) Taskset 1 (3, 6, 6), 2 (2, 9, 9)
4) Taskset 1 (2, 4, 4), 2 (4, 8, 8)
5) Taskset 1 (2, 5, 5), 2 (4, 7, 7)
6) Taskset 1 (1, 2, 2), 2 (2.5, 5, 5)
# Tasks | RM Util Bound
1 | 1.00
2 | 0.828
3 | 0.780

## Slide 3: Q2. Schedulability under RM, DM, or EDF
Determine schedulability of the following tasksets under (1) Rate Monotonic (RM) scheduling, using Utilization Bound test and/or Response Time Analysis (RTA) to determine taskset schedulability. (2) Deadline Monotonic (DM) scheduling (3) Earliest Deadline First (EDF) scheduling, using Utilization Bound test.
1) Taskset
2) Taskset
3) Taskset

## Slide 4: Q3. RM, EDF, LLF
RM |  |  |  |  |  |  |  |  |  | 
EDF |  |  |  |  |  |  |  |  |  | 
LLF |  |  |  |  |  |  |  |  |  | 
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Gantt Chart
Task ID | T=D | C | RM Resp. Time | EDF Resp. Time | LLF Resp. Time
1 | 8 | 3 |  |  | 
2 | 10 | 4 |  |  | 
Time | τ₁ Laxity | τ₂ Laxity | Running Task
t=0 |  |  | 
t=1 |  |  | 
t=2 |  |  | 
t=3 |  |  | 
t=4 |  |  | 
t=5 |  |  | 
t=6 |  |  | 
t=7 |  |  | 
t=8 |  |  | 
t=9 |  |  | 
Consider the set of 2 periodic tasks whose period, deadline and WCET parameters are given.
1. For each scheduling algorithm (RM, EDF, LLF), draw the Gantt chart by filling in the table with the task ID that runs in each time slot until time 10, and calculate the WCRT for each task.
2. Under RM scheduling, use utilization bound and Response Time Analysis (RTA) to determine taskset schedulability.